## Slide 1: Recycling Identification System for Public Waste Management
Shivam Singh, Mark Glinberg, Nityam Bhachawat

## Slide 2: Setup
Metal Container
  Paper inside to block reflections
Raspberry Pi
Camera
Load Sensor
2 UWB Sensors
Code and Files:
  https://github.com/specialsyt/recycling-identification-system
Load Sensor Platform
UWBs
Load Sensor and ADC
Raspberry Pi
Camera

## Slide 3: Camera
Raspberry Pi 1080p Camera
YOLO model
  Fine-tuned on custom dataset
  Required higher fidelity images with more depth
OpenAI as a backup
  Used OpenAI API to aid with classification

## Slide 4: Load Sensor
FlexiForce A201 Sensor
  Lowers resistance when compressed, increasing the measured voltage
  Analog Pins read at 12 bits (values 0-4095), so can be scaled to voltage by v = 3.3x / 4095
3D Printed Case
Adafruit Feather M0 Express ADC
  Ran into inconsistency issues due to soldering
Output ADC value and Voltage
  Averaged 20 samples of ADC value over 1 second

## Slide 5: UWB
Modified TWR output to Channel Impulse Response (CIR)
  Measured difference in ToA of peaks
    Gives insight into object composition
    Refractive index can’t be calculated without knowing thickness
UWB setup was difficult (used outdated libraries)
  UWB sensors do not work on the Raspberry Pi
    We connected them to a laptop and sent data to the Pi
  CIR peak differences were well within margin of error, results weren’t helpful for classification

## Slide 6: UWB

## Slide 7: Methodology
Start script
Get UWB CIR with nothing there
Place Object
Get UWB CIR with object
Get load sensor reading
Get image and classify (YOLO and OpenAI)
Use all the above data points to cl assify object
  Nearest Neighbor with existing data points
  Save data point for future classifications

## Slide 8: References
https://core-electronics.com.au/guides/force-sensitive-pads-raspberry-pi/
https://www.tekscan.com/sites/default/files/resources/FLX-Datasheet-A201-RevI.pdf
https://www.adafruit.com/product/3403?gad_source=1&gclid=Cj0KCQiAuou6BhDhARIsAIfgrn6ctTSm-DQVjLh3pKMRvGc9iCZPzZIif_SJrcqGiEkxk4_SlcXT8VMaAk6DEALw_wcB